## Slide 1
SVKM’s NMIMS
Mukesh Patel School of Technology Management and Engineering, Vile Parle, Mumbai- 400056
Department of Artificial Intelligence
30/10/2026
1
Bachelor of Technology
Internship/Project
Final Presentation
Academic Year 2026–27
Semester VIII
Notes: Opening: introduce the final project presentation and institutional affiliation. The original four-by-three template, logo, background, typography and institution panel are retained. Placeholder review/year text is updated to Final Presentation and the report academic year2026–27. This deck is planned for10–15minutes. The presentation separates current source implementation, logged model validation, reported figures without raw logs, and the newly trained traffic-sign extension.

## Slide 2
30/10/2026
2
A PRESENTATION ON
SELF-DRIVING MINI CAR
Lane Detection, Obstacle Avoidance and
Traffic Sign Recognition
By
Krishna Menon | I045 | SAP: 70122300036
Aditya Rana | I059 | SAP: 70122300063
Parth Surve | I076 | SAP: 70122300089
Under the guidance of
Dr. Hima Deepthi Vankayalapati
Department of Artificial Intelligence
PERCEPTION
DECISION
CONTROL
Notes: Our project is Self-Driving Mini Car: Lane Detection, Obstacle Avoidance and Traffic Sign Recognition. The three student members are Krishna Menon, Aditya Rana and Parth Surve, under Dr.Hima Deepthi Vankayalapati. Student identifiers are taken from the uploaded final project report, not older presentation scripts in GitHub which use different roll numbers. The paper itself uses a related two-layer architecture title; that manuscript title is shown on the paper-status slide.

## Slide 3
Introduction and Problem Statement
THE PROJECT AT A GLANCE / SEE THE TRACK • CHOOSE AN ACTION • MOVE
30/10/2026
3
A small autonomy testbed
Concept illustration • skid-steer drive
How do we turn what the
camera sees into useful motion?
Perceive
Read lanes, signs and visual hazards.
Decide
Resolve instructions and safety priorities.
Act
Execute motor commands and report state.
Tools: Python / OpenCV • YOLO / NCNN • Picamera2 / pyserial • Uno C++
Sources: final report Ch. 1/3; Krishna main 9aeb238. Hardware shown here is conceptual illustration, not prototype photography.
Notes: Introduce a controlled-track autonomous RC-car project. The image is a conceptual chassis illustration, not a photograph of the team vehicle. Perception runs on Raspberry Pi5; Arduino Uno executes motor PWM and local sensing. The project combines lane geometry, visual hazard recognition and a separate trained traffic-sign extension. The core objective is coordinated and observable behavior. Specific model scores and validation boundaries are concentrated on slide12. No actual car photographs are included in this revision.

## Slide 4
Literature Review and Research Gap
WHAT PRIOR WORK ENABLES / DETECTION • TRACKING • ACCESSIBLE ROBOTICS
30/10/2026
4
Learned detection
YOLOv10 + RDD2022 [1,3]
Use compact detectors;
check the data domain.
Efficient tracking
KCF owner tracking [2]
Track between detections;
recover after target loss.
Accessible robotics
OpenBot + Duckietown [4,5]
Keep the platform modular
and the workflow reproducible.
Project contribution: connect these methods through clear decisions and embedded execution.
Sources: [1–5] on slide 16. Detection image: repository validation crop. Person and board visuals are conceptual illustrations.
Notes: The literature informs individual design choices rather than proving this prototype superior to other robots. YOLOv10 provides the object-detection family, KCF supports inexpensive visual tracking, and RDD2022 provides a road-damage learning task. OpenBot and Duckietown demonstrate accessible educational autonomy. Our focus is the interface between perception and actuation: clear serial commands, finite-state execution and complementary sensing. We do not reproduce unsupported comparative latency or accuracy numbers from secondary report tables. Full citations and the repository revision appear in the references slide and notes.
Viva: novelty is at the system-integration level, not a new object-detection architecture. Explain why KCF complements neural detections and why RDD scores cannot be transferred to a model-car printout track. There is no controlled comparative benchmark establishing superiority over OpenBot or Duckietown. OpenBot is an ECCV2020 work; this corrects the venue in the supplied report.

## Slide 5
System Architecture / Block Diagram
ILLUSTRATED ARCHITECTURE / FOLLOW THE CAMERA-TO-MOTOR PATH
30/10/2026
5
PERCEPTION / DECISION
EMBEDDED CONTROL
state
CSI camera
Live frames
Raspberry Pi
See + decide
Arduino Uno
Sense + execute
L298N driver
Motor power
Serial
Front sonar
feeds Uno
Dashboard
Live view + status
Commands travel to Uno; telemetry returns to Pi. Sonar is read on Uno, not through Pi GPIO.
Source: Krishna main 9aeb238 runtime and firmware. Component art is illustrative; arrows show functional interfaces, not physical wiring.
Notes: The component pictures are generated conceptual illustrations, not photographs of the installed boards and not a pin-level wiring schematic. Follow CSI camera→Pi→serial→Uno→L298N→paired motor sides. Sonar echo timing terminates on Uno. The Pi consumes returned distances and state. Serial is115200baud. Pi runs lane geometry, general YOLO hazards, dedicated pothole recognition and tracking; the sign model extends its decision stage separately from Krishna main. Uno executes finite-state motion and local avoidance. The illustration does not prove board port placement, power wiring, metric odometry or measured heading. Current firmware and sketch-local pins are the wiring authority. Ordinary USB is not galvanic isolation.
Hardware reference: left motor B=D6PWM/D10/D11; right A=D5PWM/D8/D9. Left sonar=D7TRIG/D13ECHO; right=D12TRIG/D4ECHO. D2/D3 reserved for future encoders. Camera CSI; serial115200baud. Pi Python stack: Picamera2, OpenCV, Ultralytics/NCNN, pyserial. Uno uses C++ motion-state control.

## Slide 6
Methodology / Decision and Safety Flow
ARBITRATION / ONE COMMAND OWNER AT A TIME
Sources: car/main.py; Uno motion FSM; Traffic Sign/car/main.py and TrafficSignPolicy (separate trained extension).
30/10/2026
6
Capture frame + telemetry
Hazard or safety latch?
YES
STOP / existing avoidance
NO
STOP / No Entry hold?
YES
Hold + dashboard message
NO
Confirmed turn + clear?
YES
Bounded sign maneuver
Lane / follow / reactive guidance
OBSERVE
Only fresh sensing
can authorize a
sign maneuver.
RE-EVALUATE
Interruption during
a sign turn → stop
and fault. Uno local
safety can preempt.
Sign extension: observations ≤0.75 s old; sonar ≤0.8 s; obstacle results ≤0.5 s.
Notes: The control loop first captures a frame and drains incoming telemetry. General neural detection is scheduled every third loop iteration; cached boxes are reused in between, so loop FPS is not fresh neural FPS. In the trained extension, sign inference is separately rate-limited. Existing obstacle decisions retain priority when no sign action is active. A STOP or No Entry hold suppresses ordinary driving; a turn requires confirmation and clearance. If a hazard interrupts an active sign maneuver, it stops and records a fault. Normal lane, person-following or reactive guidance proceeds only when no higher-priority action governs the iteration.
Flowchart is a conceptual priority view: exact branches are implemented in the runtime, including obstacle-specific stop/bypass choices. In particular, a pending sign does not force a turn through an obstacle. A turn already active that is interrupted becomes a fault instead of silently resuming. Freshness checks apply to the trained extension; do not claim those exact checks were already present in Krishna main. Default three confirmations must be fresh detector observations, never the same cached bounding box repeated three times. The independent Uno local avoidance layer remains operative.

## Slide 7
Use Cases / From Operator to Outcome
BEHAVIOR CONTRACT / WHAT THE USER ASKS AND THE CAR MUST DO
Sources: repository dashboard routes and operating modes; trained sign policy; conceptual UML diagram.
30/10/2026
7
AUTONOMOUS RC CAR
Operator
Track / signs
Select mode / owner
View state / stop / reset
Lane / person guidance
Hazards / sign response
Visual event
Policy state
Command
Motion
A complete demonstration pairs the detected event with policy state, commands and observed movement.
Notes: This use-case view distinguishes the human operator from the environment. The operator selects a mode, chooses the owner for follow mode, inspects telemetry and can stop or reset the system. The environment supplies lane markings, people, obstacles and printed signs. The system uses the same perception-control boundary across these tasks. Resetting the traffic-sign policy does not release an independent emergency latch. Direct manual motion is deliberately restricted while sign arbitration owns movement. The diagram represents supported interactions; it is not a claim that all physical scenarios have passed track validation.
Use-case diagram is conceptual UML, not a component wiring diagram. Operator actions include mode selection and choosing a follow-me owner. The environment is a source of lanes, people, signs and obstacles. A demonstration should log the visual event, policy state and command, then independently observe movement. Emergency stop and traffic-policy reset are different operations; resetting No Entry cannot release an unrelated safety latch. Actual-track outcomes are pending, so the bottom table is a demonstration plan, not claimed test results.

## Slide 8
OBSTACLE AVOIDANCE / VISUAL HAZARDS + FRONT SONAR → MOTION PRIORITY
30/10/2026
8
Obstacle Detection / Avoidance Logic
SCHEMATIC CAMERA CORRIDORS
LEFT
CENTER
RIGHT
HAZARD
Vision
Sonar
Illustrative bypass
when clearance permits
Detect candidate hazards
YOLOv10n object boxes join person and pothole detections.
Assess the path
Score left, center and right using box geometry, confidence and front sonar.
Choose the motion
Close central danger → STOP; otherwise slow or bypass toward a clearer side.
Safety arbitration takes priority over normal lane / follow guidance; Uno reflex states retain control.
Sources: car/main.py _check_obstacle_ahead and mode handlers; perception/avoidance.py, Krishna main 9aeb238. Drawing is conceptual.
Notes: Source-backed obstacle path: general YOLOv10n detections plus person/pothole boxes feed _check_obstacle_ahead and compute_zone_scores. Central corridor is20–80% of image width; box-height fraction above0.40 requests camera STOP, above0.15 requests caution. The camera stop is latched with PI_STOP; release behavior is mode-specific, including guarded autonomous escape logic, so do not imply an unconditional permanent latch. Zone scoring considers confidence, obstacle class weight, area, bottom-edge proximity and front ultrasonic ranges; image position is a proximity heuristic, not calibrated meters. Left/center/right danger chooses the lower-risk lateral direction, or STOP when blocked. Autonomous bypass sends PI_AVOID plus a timed±35degree turn atPWM160; lane mode uses±32degrees at lane curve speed. Asymmetric sonar can also request bypass; critical front range uses25cm threshold in the Pi config. Respect Uno AVOIDING/CLIFF_REVERSING states; the source supports cliff behavior but the diagram is not proof of validated cliff sensing. The detailed avoidance helper has extra actions, but main imports decide_avoidance, not decide_avoidance_detailed. No new physical avoidance success rate is claimed. Exact hardware pins remain in architecture notes and the companion guide.

## Slide 9
Lane Detection / Geometry to Steering
CLASSICAL VISION / TRACK STRUCTURE WITHOUT ANOTHER NEURAL MODEL
Sources: lane_detector.py and config.py, Krishna main 9aeb238. Diagram is illustrative image-space geometry, not a captured test.
30/10/2026
9
Yellow: boundaries • teal: desired center
1 Mask + isolate
2 Fit + stabilize
3 Guide + recover
IMAGE SPACE • TRACK REGION
Lookahead row
Mask lane colors in the lower-frame region.
Exclude overlapping hazard boxes.
Sliding-window pixel search → robust curves.
Smooth across frames; reject sudden jumps.
Estimate center from both lines or one.
Guide motion; prolonged lane loss → STOP.
Steer toward the lane center
while respecting the path direction.
Lane geometry supplies direction; confidence and loss handling determine when guidance can continue.
Notes: Lane detection is classical image processing, not a YOLO lane model, so an mAP score is not applicable. The pipeline examines the lower55percent of the frame, masks supported line colors, excludes hazard bounding boxes, tracks window pixels and robustly fits quadratic boundaries. A center trajectory can be recovered temporarily from one line. Lookahead is configured at0.68of image height. The implementation applies smoothing and rejects large geometry jumps. If the lane is missing beyond eight frames, it stops rather than inventing a path. The drawing is schematic, not a calibrated metric road model or an accuracy result. Timing claims in context documentation require device logs for verification.
Equation uses normalized image coordinates, not meters. Center-path tangent is ψ = −atan(2ay+b), converted to degrees. Code applies proportional lateral-error gain145 and tangent gain28/45, then clips to±38degrees. Despite the source describing this as pure pursuit, this slide states the implemented algebra rather than asserting a calibrated vehicle bicycle model. Steering deadband is6degrees; speeds default165 straight and145 correction PWM. ROI starts0.45H; lookahead0.68H; default lane width0.52W. Lane geometry has no detector mAP. Appropriate real-track metrics are lateral error, completion rate, intervention count and cycle time.

## Slide 10
Pothole Detection / Learning and Decisions
FROM VISUAL HAZARD TO RESPONSE / A MODEL OUTPUT YOU CAN EXPLAIN
30/10/2026
10
Actual logged prediction on a printout
Detect road damage
D40 model adapted to printed
road-damage scenes.
Filter candidate boxes
Apply confidence and lower-image
checks to accept relevant boxes.
Choose a safe response
Feed boxes into stop / bypass logic;
sonar adds proximity information.
Road-damage and printout validation are different domains; their logged scores are shown together on the results slide.
Sources: detector.py; printout_gpu_pothole_model/val_batch0_pred.jpg, Krishna main 9aeb238. This is logged model output, not track-test proof.
Notes: The live source loads a dedicated pothole model in addition to the general YOLOv10n obstacle model. The classical Laplacian routine remains available but is off by default, so we do not describe it as always active. The original RDD run has50logged epochs and finalmAP50of0.25226. The printout fine-tuning log in the current repository contains six recorded epochs, ending at0.97333mAP50. Although its arguments request25epochs, only six rows are evidence. The uploaded report expresses uncertainty about the printout result; the newly fetched CSV establishes the logged value, but not external validity or independence of the split.
Both plots show actual logged validation points, with a shared0–1vertical scale but separate domains and epoch counts. The inset is the top-right cell of the repository val_batch0_pred.jpg montage, shown using editable PowerPoint crop metadata; its prediction boxes are preserved. Final CSV values are used consistently; RDD best mAP50is0.25410 at epoch49, while final epoch50is0.25226. Printout args request25epochs but the CSV contains6rows. mAP50is mean average precision at IoU0.50; mAP50–95 averages IoU thresholds0.50through0.95. The printout score establishes logged validation performance, not an audited independent split or physically observed avoidance success. Confidence threshold is0.20 in current config for potholes.

## Slide 11
Traffic Signs / Train → Confirm → Act
FOUR-CLASS TRAINED EXTENSION / DELIVERED SEPARATELY FROM KRISHNA MAIN
Sources: Traffic Sign/MODEL_CARD.md, heldout_summary.json, action_check_ncnn.json and main.py / traffic_sign_policy.py.
30/10/2026
11
STOP
Stop dwell: 3 s
NO ENTRY
Hold until reset
LEFT
Bounded left turn
RIGHT
Bounded right turn
TRAINING / ACTUAL ARTIFACTS
1
2
3
Lane mode: bounded pulses + reacquisition
Four road-sign classes
Varied synthetic scenes
Fine-tuned YOLOv10n
Lightweight NCNN deployment
Confirm across fresh frames
Reject stale or weak predictions
Check size and image position
Act only when the sign is suitably visible
Clearance → bounded action
Camera frame → sign recognition → safety checks → action and dashboard feedback.
Notes: Traffic-sign recognition is the trained extension developed in this conversation and supplied separately; it is not yet on Krishna main9aeb238. The four demonstrated prints are STOP, No Entry, Left and Right. We actually fine-tuned YOLOv10n for25epochs on generated sign images, and exported verified FP16NCNN weights. The held-out synthetic mAP50is0.99486; it must not be presented as real road accuracy. The extension confirms three fresh observations. STOP commands a dwell; No Entry holds until reset; turns use apparent size and bearing plus safety clearance. Both checkpoint and NCNN passed all four image-to-command checks with mocked motors. One SLOW octagon falseSTOP and one unfamiliar small-font miss remain recorded.
The sign model is genuinely trained; it is not template matching and does not require a video file at runtime. It accepts frames from the moving camera. Synthetic backgrounds, geometry and card placement vary; held-out counts are image counts, not independent physical trials. No flips are used because mirroring arrows changes their meaning. NCNN and PT checks both produce the four expected policy outcomes. A known negative SLOW octagon gives a falseSTOP; an unfamiliar narrow-font smallSTOP can be missed. Turn gate assumes53.5degree horizontal FOV, uses a pinhole bearing estimate, and is not a junction detector or metric distance. Default turn PWM210; calibration10ms/degree. Lane-mode turn pulses12degrees, requires commanded motion≥72degrees plus lane departure and three fresh centered DUAL_LOCKED frames; cap96commandeddegrees or6seconds leads to a fault if not completed. Autonomous/follow modes use timed±90degree commands; actual heading is not verified.

## Slide 12
Result Analysis / Scores and Verification
MODEL METRICS / MEASUREMENTS AND VALIDATION SCOPE
Sources: GitHub CSVs at 9aeb238; separate sign extension validation JSON; no dated physical Pi performance log supplied.
30/10/2026
12
Evaluation domain | Precision | Recall | mAP50 | mAP50–95
RDD2022 road damage | 0.53992 | 0.27092 | 0.25226 | 0.11421
Pothole printout run | 0.99902 | 0.95506 | 0.97333 | 0.70171
Traffic signs: synthetic | 0.98462 | 0.99896 | 0.99486 | 0.97783
WHAT IS VERIFIED
WHAT NEEDS TRACK MEASUREMENT
• Logged validation scores and training curves
• Four sign image-to-command outcomes
• Lane algorithm and software thresholds
• Lane error / route completion rate
• Camera-to-motion delay and braking distance
• Sustained fresh-inference FPS on Pi
Loop FPS ≠ fresh detection FPS. General neural detection runs every third loop iteration.
Notes: Read the rows by domain, not as a ranking. The road-damage model has substantial limitations, especially recall, while the printout validation is much easier and narrower. The traffic model was evaluated on synthetic imagery. Precision and recall here are evaluator summaries, not a guarantee for every camera frame. The report lists38msor26.3FPSandother sections claim22–26ms, but explicitly states raw device timing logs are absent. The software also runs neural detection every third loop iteration. Therefore the presentation makes no independently verified20–30fresh-detectionFPSclaim and no physical stopping-distance guarantee. A waveform or scenario table alone is not proof of measured latency.
Metric definitions for viva: precision=TP/(TP+FP), recall=TP/(TP+FN). AP is area under the precision–recall curve; mAP averages per-class AP. IoU=intersection area / union area. Confidence is not an accuracy percentage. These three rows cannot be compared as competing models because their tasks and data domains differ. Inference frequency is bounded by scheduling and contention; sign inference is separately rate-limited. An end-to-end latency budget must include capture, preprocessing, inference, arbitration, serial transmission and physical actuation. Do not quote reported26.3FPS as reproduced on-device evidence.

## Slide 13
Conclusion and Future Scope
DELIVERED CAPABILITY / A CLEAR PATH TO STRONGER PHYSICAL EVIDENCE
Sources: final report conclusion and limitations; current source code; trained sign extension reports.
30/10/2026
13
Pi
Separate workloads
Pi for perception; Uno for
actuation via an explicit
serial command interface.
CV
Fuse complementary cues
Lane geometry and learned
hazards, complemented by
nearby-obstacle sonar.
UI
Make actions observable
Signs and motion states
appear as dashboard feedback
for observable decisions.
NEXT EXPERIMENTS
•
Measure
Latency + braking
•
Calibrate
Turn + camera geometry
•
Generalize
Real photos + rear sensing
Next hardware step: encoders / completed IMU feedback for measured motion instead of timed estimates.
Notes: The outcome is a modular prototype with a clear division of responsibility and reproducible software artifacts. Its main contribution is coordination, not proof that a small camera can safely drive on public roads. Future work should start with dated physical logs: camera-to-command delay, sonar update behavior, actual braking distance and sustained Pi temperatures. Rear sensing addresses reverse blind spots. Encoders or a completed IMU heading implementation are needed for measured turns rather than time estimates. Real photographs of printed signs, potholes and track conditions should be added to training and independently evaluated. These are future capabilities, not features already verified.
Present the work as an educational controlled-track prototype with delivered implementation and reproducible training evidence. Critical next measurements: synchronized camera-to-command timestamps, physical stopping distance versus speed, sustained temperature and inference throughput, track intervention count, lane position error and real printed-sign sensitivity. New datasets should be split by physical scene/session to reduce leakage. Encoders and completed IMU feedback enable actual heading/distance estimation; current heading stub does not. Rear sensing is needed before stronger reverse-motion claims.

## Slide 14
SDG Mapping / Engineering with a Purpose
PRIMARY ALIGNMENT: SDG 9 / SUPPORTING LINKS: SDG 3 AND SDG 11
Sources: official UN targets at sdgs.un.org/goals/goal9, /goal3 and /goal11. Potential contribution, not measured societal impact.
30/10/2026
14
9
INDUSTRY, INNOVATION
& INFRASTRUCTURE
Target 9.5
Affordable robotics research.
Modular code and shared
validation artifacts.
Direct research / innovation link
3
GOOD HEALTH
AND WELL-BEING
Target 3.6
Study obstacle sensing and
stop decisions as foundations
for collision-risk research.
No injury-reduction claim
11
SUSTAINABLE CITIES
AND COMMUNITIES
Target 11.2
Explore safer mobility
technology through a small
controlled-track platform.
No deployed transport claim
Primary: SDG 9.5 research and innovation. Supporting: safety and mobility research (3.6 and 11.2).
Notes: SDG9is the primary mapping because this is an engineering research and innovation project with reproducible methods and modular hardware. SDG3target3.6is relevant to the motivation of collision prevention, but we have not measured injury reduction and cannot claim that impact. SDG11target11.2concerns safe, accessible and sustainable transport; our contribution is exploratory education and prototyping, not a deployed transit service. This mapping avoids claiming carbon savings, accident reductions or social outcomes that were never measured. The official United Nations goal pages are included as source links.
Assessment cue: explain an evidence-backed mechanism, not just a list of SDG logos. Goal9target9.5concerns research and technological capabilities and best matches the deliverables. Goal3target3.6is a safety-motivation link, not demonstrated injury reduction. Goal11target11.2is relevant to safe transport research, while our small prototype is not itself a public transportation solution. Colored number circles are project illustrations, not altered official UN logos.

## Slide 15
Paper Status Till Final Presentation
PUBLICATION PROGRESS / MANUSCRIPT → SUBMISSION → DECISION
Source: team confirmation in this chat; supplied final manuscript. Venue, submission ID and decision email were not provided.
30/10/2026
15
Autonomous RC Car Using Two-Layer Edge
Perception and Real-Time Embedded Control
✓
Manuscript prepared
✓
SUBMITTED
…
Decision awaited
Current team-confirmed status: submitted. Acceptance has not been confirmed.
Venue and decision details will be added when available.
Notes: The team states that the paper has been submitted. We have not been given the venue, submission identifier, submission date, reviewer decision or acceptance email. Consequently, this slide must not be read as acceptance. The supplied final paper is a manuscript, while the project report contains institutional approval/logbook pages, neither of which constitutes a journal or conference acceptance notice. When a genuine decision arrives, replace the status and insert the actual supporting email with private identifiers redacted as appropriate. Do not invent a venue logo, screenshot or publication identifier.
Do not say the paper is under peer review unless that status is confirmed. Submitted means only the team has stated submission; the venue, identifier and date are not available here. A manuscript PDF and institutional report approval do not constitute publication acceptance. Use an actual decision email later, with sensitive identifiers handled appropriately. This slide fulfills the paper-status requirement while retaining a truthful record.

## Slide 16
References / Reproducible Evidence
RESEARCH → CODE → MODEL LOGS / CLICKABLE SOURCES
Repository review basis: Krishna main 9aeb238. Detailed traceability and examiner Q&A are in the speaker notes and companion guide.
30/10/2026
16
METHODS
[1] Wang et al. YOLOv10: Real-Time End-to-End Object Detection. 2024. arXiv:2405.14458.
[2] Henriques et al. High-Speed Tracking with Kernelized Correlation Filters. IEEE TPAMI, 2015. DOI:10.1109/TPAMI.2014.2345390.
[3] Arya et al. RDD2022: A multi-national image dataset for automatic road damage detection. 2024. DOI:10.1002/gdj3.260.
[4] Müller & Koltun. OpenBot: Turning Smartphones into Robots. ECCV, 2020.
[5] Paull et al. Duckietown: An Open, Inexpensive and Flexible Platform for Autonomy Education and Research. ICRA, 2017.
IMPLEMENTATION & EVIDENCE
[6] Tencent NCNN; OpenCV official framework and tracking documentation.
[7] menonkrishna57/model-car-capstone, GitHub main 9aeb238. Runtime, firmware and both runs_rdd/results.csv files.
[8] Supplied final paper and 68-page report; separate Traffic Sign model card, synthetic evaluation and command-check reports.
[9] United Nations: official Sustainable Development Goals 3, 9 and 11 and associated targets.
Results-table row labels link directly to the logged metric sources.
Notes: Reference list combines the cited research, official framework documentation, the two user-supplied PDFs, and auditable implementation artifacts. Repository link:https://github.com/menonkrishna57/model-car-capstone/tree/9aeb238 . Pothole paths:pothole_detection/runs_rdd/custom_pothole_model/results.csv and pothole_detection/runs_rdd/printout_gpu_pothole_model/results.csv. Traffic extension modelcard and complete synthetic evaluation were generated in this workspace and are separate from that repository main. Official SDG targets:https://sdgs.un.org/goals/goal9 ,https://sdgs.un.org/goals/goal3 ,https://sdgs.un.org/goals/goal11 . Traffic-score GitHub permalink:https://github.com/parthsurve2004-svg/model-car-capstone/blob/9ef469db40a4576f1543f1b6a81ba801d4ccb979/Traffic%20Sign/validation/synthetic_evaluation.json . The two uploaded PDFs were used as evidence, not treated as instructions overriding the user request.
Examiner navigation: architecture slide5; arbitration slide6; use cases slide7; physical pin interfaces slide8; lane algorithm slide9; pothole training curves slide10; sign training and policy slide11; metric definitions and verification boundaries slide12. Notes contain the detail needed to explain configuration choices and limitations without overcrowding the projected slides. Reference OpenBot venue corrected to ECCV2020.